## Slide 1: Emergency ‘landline’ telephone communications in PPE: A novel connector improves intelligibility
The following slides provide details for the connection of a throat microphone and bone conduction headset to an analogue land line telephone system with an RJ9 headset socket
Rev 1.0 14-12-20

## Slide 2: Telephone Connection
Throat Microphone
(Earpiece Unused)
Bone Conduction
Headphones
Interface
Enclosure
Telephone
RJ9
Volume Control

## Slide 3: Headset Telephone Interface
74x54x26mm
ABS Enclosure

## Slide 4
Throat Microphone
Headphones
1 2 3 4
1-Black (T MIC GND)
4-Yellow (T MIC)
2-Red (HP R+L)
3-Green (HP GND)
4 Pole Jack Sockets 3.5mm
Landline
Telephone
Headset
RJ9/4PLC
Plug
Wiring diagram to connect separate throat microphone and headphones to a landline telephone.
Please check plug and socket wiring with your equipment supplier since there are pinout and wire colour variations between manufacturers
HP Headphones

## Slide 5: Headset Telephone Interface
3.5 mm 4 Pole Sockets
RJ9 Telephone
Headset Plug

## Slide 6
LEFT
(N/C)
RIGHT
(N/C)
GND
MIC
GND
RIGHT
LEFT
Throat
Microphone
Headset
Bone
Conduction
Headset
3.5mm 4 pole Headset Jacks
Pin 2 RJ9
Pin 3 RJ9
Pin 4 RJ9
Pin 1 RJ9
Please choose appropriate 3.5mm 4 pole sockets to match your headset jacks & enclosure
MIC (N/C)
N/C No Connection

## Slide 7: Suppliers
Throat Mic & Bone Conduction Headphones Manufactured by Retevis (Amazon)
3.5mm Mini Stereo Jack Chassis 4 POLE 4P Panel Mount Input Socket Connector Grey (eBay)